## Slide 1: W3C WoT Standardization
W3C WoT Open Day, Munich, Germany, 3 June 2019

## Slide 2: Internet of Things
Interconnecting devices and services to blend the physical world and virtual world
10
01
11
01
10

## Slide 3: Industrial Internet of Things
Connecting OT with IT
10
01
11
01
10

## Slide 4: Industrial Internet of Things
Who are you?
Name, ID, type, location, ... general metadata ...
What data and functions?
Input, output, type, range, unit, ... semantic meaning ...
How to interact?
Protocol, address, payload format security mechanism, ... interaction model ...
What else?
Manual, spare parts, digital twin, ... related entities ...
10
01
11
01
10
Web Technology
URIs, HTTP, JSON, REST, Linked Data, ... , usability!

## Slide 5: W3C WoT Building Blocks
WoT Security and Privacy Guidelines
Web Things
WoT Architecture
WoT Scripting API
WoT Binding Templates
WoT Thing Description
Information model and representation format for rich semantic metadata
“The HTML for Things”
JavaScript runtime environment similar to Web browser, but for IoT applications
Include existing ecosystems
Overarching security guidance with the prudence level of the World Wide Web
Metadata
Actions
Properties
Events

## Slide 6: WoT Thing Description (TD)
JSON-based document that is also machine-understandable (JSON-LD)
{
"@context": "https://www.w3.org/2019/wot/td/v1",
"id": "urn:dev:ops:32473-WoTLamp-1234",
"title": "MyLampThing",
"securityDefinitions": {"dflt": {"scheme": "basic"}},
"security": "dflt",
"properties": {
"status": {
"type": "string",
"forms": [{"href": "https://mylamp.example.com/status"}]
}
},
"actions": {
"toggle": {
"forms": [{"href": "https://mylamp.example.com/toggle"}]
}
},
"events": {
"overheating": {
"data": {"type": "string"},
"forms": [{
"href": "wss://mylamp.example.com/oh",
}]
}
},
"links": [{
"rel": "describedby", "href": "https://docs.example.com/WoTLamp"
}]
}
WoT Thing Description
Information model and representation format for rich semantic metadata
“The HTML for Things”

## Slide 7: WoT Thing Description (TD)
With context extensions for semantic annotations (e.g., SAREF, eCl@ss)
WoT Thing Description
Information model and representation format for rich semantic metadata
“The HTML for Things”
{
"@context": ["https://www.w3.org/2019/wot/td/v1", {
"@language": "en",
"saref": "https://w3id.org/saref#",
"eco": "http://www.ebusiness-unibw.org/ontologies/eclass/5.1.4/#"
}],
"@type": ["Thing", "eco:C_AKJ644003-gen"],
"id": "urn:dev:ops:32473-smart-machine-0815",
"title": "Smart Manufacturing System",
"description": "Entry point Thing with high-level controls",
"version": {"instance": "1.2.3"},
"support": "mailto:support@example.com?subject=Smart+Manufacturing",
"securityDefinitions": {"tokens": {"scheme": "bearer"}},
"security": "tokens",
"eco:P_BAA001001": "Acme Corporation",
"properties": {
"operatingMode": {
"@type": "saref:MultiLevelState",
"description": "The current mode of the manufacturing system",
"readOnly": true,
"type": "string",
"forms": [{
"op": "readproperty",
"href": "opc.tcp://192.168.0.1:4840?ns=3;s=System.Mode",
"contentType": "application/json"
}]
},
"manufactured": {
"@type": "saref:Measurement",
"description": "The number of produced boxes",
"readOnly": true,
"type": "integer",

## Slide 8: Innovation of WoT TDs
TD
WoT Thing Description combines three distinct, complementary technologies

## Slide 9: Innovation of WoT TDs
Protocol Bindings
Semantic Annotations
Data Schemas
TD
JSON Schema
Description of existing data formats
Validation of payloads through available implementations
Already in use by industry, e.g., OpenAPI (microservices), Open Connectivity Foundation

## Slide 10: Innovation of WoT TDs
Hyper-media
Semantic Annotations
Data Schemas
TD
JSON Schema
Description of existing data formats
Validation of payloads through available implementations
Already in use by industry, e.g., OpenAPI (microservices), Open Connectivity Foundation
Web Links and Forms
Uniform REST interface to describe IoT protocol bindings applicable to HTTP and CoAP, but also MQTT, Modbus, UA Binary, et al.
URIs to identify the IoT protocol and the target address
Media Types identify the payload format (e.g., application/json)

## Slide 11: Innovation of WoT TDs
Hyper-media
Semantic Annotations
Data Schemas
TD
JSON Schema
Description of existing data formats
Validation of payloads through available implementations
Already in use by industry, e.g., OpenAPI (microservices), Open Connectivity Foundation
JSON-LD 1.1
Linked Data and reasoning makes TDs machine-understandable
Agree on semantic meaning through controlled vocabularies
Reuse Semantic Web vocabularies and ontologies such as SAREF or eCl@ss and JSON-LD implementations for knowledge graphs
Web Links and Forms
Uniform REST interface to describe IoT protocol bindings applicable to HTTP and CoAP, but also MQTT, Modbus, UA Binary, et al.
URIs to identify the IoT protocol and the target address
Media Types identify the payload format (e.g., application/json)

## Slide 12: What Is Next?
Hyper-media
Semantic Annotations
Data Schemas
TD
Propagate this innovation
W3C WoT is promoting TD in other consortia and seeks new collaborations and wider participation
e.g., a new alliance envisions one data model, which W3C WoT started to implement 2.5 years ago
Grow semantic vocabularies
A W3C Community Group was formed to develop the necessary IoT extensions for schema.org
Gain more implementation and field experience
Establish the WoT building blocks in the verticals and leverage the network effect to foster
convergence in the IoT

## Slide 13: W3C WoT Standardization
W3C WoT provides four building blocks to describe IoT devices and services and to complement existing platforms and standards
  WoT Thing Description
  WoT Binding Templates
  WoT Scripting API
  WoT Security and Privacy Guidelines
WoT Thing Description combines three distinct, complementary technologies to enable semantic interoperability for the IoT
  Data schemas to describe and validate what data a Thing provides and accepts
  Hypermedia controls to describe how to interact and what else is related
  Semantic annotations to enable clear, machine-understandable metadata
10
01
11
01
10
11
00
01
11
10
11
01
01
10
11
100010101110011011
10
01
11
01
10
11
00
01
11
10
11
01
01
10
11
1000101011100110110001001001
100111011011000111101101011011100010101110011011001
010110111000101011100110111001110110110001111011010110111000101011111

## Slide 14: Contact
Dr. Matthias Kovatsch
Principal Researcher W3C WoT WG+IG Co-chair
Huawei Technologies
German Research Center
Applied Network Technology Lab
matthias.kovatsch@huawei.com